## Slide 1: RE4volution: How to build a fully recycled house demos from Italy, UK, Spain and Taiwan
Aurora María Casado Barrasa, ACCIONA
Notes: Hello, good afternoon all. I’m María Casado and I work as a Project Manager in the Technological Research Department of ACCIONA Construction.
I’m going to talk about how to build a fully recycled house based on the experience gained so far from the demonstration activities of the RE4 Project.

## Slide 2: Content
The challenge
Overview of the demo sites
Benefits of RE4 prefabricated construction
Notes: This is the outline of my presentation.My talk is divided in 5 parts. The challenge, our approach to address the challenge, the RE4 building elements developed in the Project with CDW, the work done so far in each demo and finally I will close my talk with the benefits of RE4 prefabricated construction as conclusion.
I would be happy to answer your questions at the end of my presentation.

## Slide 3: The challenge
In a circular economy, how could we have a completely recyclable building?
How do we recycle building materials in a way that we could really benefit from?
Notes: Starting with the challenge, in a circular encomony, how……. And how do we recycle buidling materials ……?

## Slide 4: How could we have a fully recyclable building?
Modular/easy assembly
To design and develop solutions for modular/easy assembly & disassembly of eco-friendly prefabricated elements.
Prefabricated construction
Easy disassembly
Design for deconstruction (reversible structural connections)
Eco-friendly elements
Building elements made with CDW
Notes: How does RE4 project address the challenge just mentioned? Through the development……
Modular and easy installation means to use prefabricated construction
Easy disassembly means design for deconstruction
And eco-friendly elements means to develop building elements made from CDW
These three targets have been covered along the project

## Slide 5: What does CDW recycling really mean?
CDW MINERAL FRACTION
Recycled aggregates
(fine and coarse fraction)
Recycled sand
RE4 concrete precast elements
RE4 concrete precast components
Structural
wall panels
RC Beams & columns
Sandwich panels (loadbearing & non-loadbearing)
RC slabs
Blocks
100% reusable (reversible connections)
Recyclable
50-100% CDW
Extruded concrete tiles
100% reusable
RE4 extruded façade panels
75% CDW
85% CDW
Notes: What does CDW recycling really mean? Here you case see which elements and components have been developed in the Project with CDW.
Concrete elements with CDW aggregates: loadbearing and non-loadbearing sandwich panels; loadbearing wall panels, beams, columns, floor slabs, and stairs; The replacement rate of virgin aggregates with recycled aggregates ranged from 50% to 100%
Concrete components with CDW aggregates : non-loadbearing blocks; In this case, the replacement rate of virgin aggregates with recycled aggregates was 75%
Façade panels with CDW sand : extruded concrete tiles made where the replacement rate of virgin sand with recycled sand was 85%

## Slide 6: What does CDW recycling really mean?
CDW LIGHTWEIGHT FRACTION
Wood scraps
100% CDW
RE4 insulating panels
100% reusable
CDW TIMBER
Recycled timber
Non-structural façade panel
RE4 timber elements
Internal partition wall with RE4 earthern plaster
100% reusable
Notes: Insulating wood panels with wood scraps coming from the lightweight fraction of the CDW.
Timber elements with recycled timber : non-structural façade panel; internal partition Wall with earthern plaster
All the mentioned building elements are 100% reusable with the exception of the building blocks which are 100% recyclable.

## Slide 7: Overview of the demo sites
Cold scenario
Warm scenario
High replication potential outside EU
Notes: The following two slides show an overview of the demo sites.
The demonstration activities for new construction will be carried out in parallel in two different European climatic scenarios, Spain (warm scenario) and Northern Ireland (cold scenario).
Demonstration of the high replication potential of the RE4 solutions outside EU will be shown trough the installation of a concrete precast panel in Taiwan.

## Slide 8: Overview of the demo sites
Notes: The refurbishment will be demonstrated in

## Slide 9: Overview of the demo sites
Assembly of the RE4 ventilated façade made of insulating wood panels and extruded tiles in an existing façade.
DEMO FROM ITALY, BENEVENTO- REFURBISHMENT (1/2)
RE4 ventilated façade
RE4 Insulating Wood panels
100%CDW
Extruded concrete tiles
85% CDW
+
Notes: The following slides describe each demo and the progress so far.
Starting from the demo from Italy, The main goal of this demo is to demonstrate and validate selected RE4 elements for refurbishment. To this end, a ventilated facade was made of xxxxx was installed in an existing wall.

## Slide 10: Overview of the demo sites
Existing wall façade
Insulating wood panels installation
Steel rails installation
Autoclaved Aerated Concrete (10cm)
Cement plaster (1cm)
Finish based on lime and cement (1cm)
Wood insulating panel (14cm)
Air cavity (10cm)
Extruded tiles (2,5cm)
U-value
= 1,1 W/m2k
Calculated U-value = 0,23 W/m2k
Before refur.
After refur.
DEMO FROM ITALY, BENEVENTO- REFURBISHMENT (2/2)
Extruded tiles assembly
Notes: Here you can see some illustrations of the construction steps carried out in the Italy demo site. The first figure is the existing wall which is made of xxxxx and has a calculated U value of …. The first construction step was to install two layers of insulation and then the steel rails were assembled to support the extruded tiles. After the refurbishment the wall with the ventilated façade has a calculated U value of 0,23, which is better than the limit value for refurbishment according to the Italian legislation (0.40)

## Slide 11: Overview of the demo sites
DEMO FROM UK, TOOMEBRIDE – NEW CONSTRUCTION, COLD SCENARIO
Foundations with upstands for services and connections for precast concrete loadbearing sandwich panels;
Ground floor loadbearing sandwich panels and stairs;
1st level slabs with anchorage to walls;
1st floor perimeter walls;
2nd Level flooring with ties to walls;
Roofing and partition walls;
Services, windows, doors and finishes
1. & 2.
3. & 4.
5. & 6.
CONSTRUCTION STEPS:
7.
50-100% CDW
Notes: Moving to the demo from UK, the main objetive of this demo is to buit a new demo building to demonstrate selected RE4 prefabricated elements in a cold climate .
As you can see from the top picture, this demo building will be quite big and will be made of RE4precast concrete components, mainly loadbearing sandwich panels, hollow core slabs , partition walls and stairs.
The next steps are the construction of the demo building. The construction steps are the following:

## Slide 12: Overview of the demo sites
DEMO FROM SPAIN, MADRID – NEW CONSTRUCTION, WARM SCENARIO
Prefabricated energy-efficiency building concept / Calculated U-value= 0.30 W/m2k
Designed for easy assembly and disassembly (reversible structural connections)
Prefab elements & components incorporating CDW (replacement rate 50-100% CDW)
Notes: On this slide, we have some pictures of the demo building built in Spain. The objetive of this demo is to buit a new building to demonstrate selected RE4 prefabricated elements in a warm climate .
In this building most of the RE4 building elements with CDW (xx, xxxxx) were assembled. It is important to remark that special emphasis has been put to reversible structural connections to tie together all the RE4 elements and facilitate the dismantling.
The wall constructions, omitting any openings, and assuming standard surface heat transfer coefficients, equates to a U-value of approximately 0.30 W/m2K, which is more stringent than the maximum U-value established by the CTE, which is 0.66W/m2K.

## Slide 13
Notes: Now I’m going to show you a short time-lapse video of the construction of both this buidling. Cutting-edge example of construction for easy assembly & disassembly and reuse

## Slide 14: Overview of the demo sites
Panels positon
DEMO FROM TAIWAN, EGA House
Steel mold before casting concrete
Concrete panel with 40% CDW aggregates
Connection details
Notes: Finally, the last demo is the demo from Taiwan . The objective of this demo is to demonstrate the high replication potential of the RE4 solutions outside EU. So far two concrete panels in which 40% of the virgin coarse and fine aggregates was replaced by recycled aggregates will be installed in a house called MEGA house which was built by the National Taiwan University of Science and Technology

## Slide 15: Benefits of RE4 prefabricated construction
Fast and easy assembly;
Easy disassembly;
Less waste ;
Cost savings in terms of collective protective measures;
Great way to save money and the environment
Notes: To conclude, I would like to tell you about the benefits of RE4 prefabricated construction.
It allows a fast and easy assembly
As well as an easy
It implies less waste
And cost savings …
It’s a great way to save money and the environment;

## Slide 16: Thank you for your attention
Aurora María Casado Barrasa
auroramaria.casado.barrasa@acciona.com
Notes: That’s all from my side. Do you have any questions?